## Slide 1: Arduino Workshop #2
Digital and Analog Inputs
Notes: 24 – Arduino Uno
24 - Small bread board
24 – Jumper wire sets
24 - 10 kΩ potentiometer
48 – 10 kΩ resistor
72 – 220 Ω resistor
24 – USB cables
24 – photoresistors
24 - TMP36 temperature sensor (or any other 5 V analog sensor)
24 – 5mm common-cathode RGB LED

## Slide 2: Reading Digital Inputs

## Slide 3: PowerPoint and Code
Github.com/EELabMan
Go To Repositories and find Arduino 2 Digital and Analog Inputs

## Slide 4: Wire diagram

## Slide 5: Pull down resistor
Notice the resistor running from the button to the ground
  This is a pull down resistor
    5 v can run two paths
      When the button is not being pressed it runs through the resistor to ground
      When the button is pressed it runs through the button to ground
    This insures that
      The button does not create a short
      The input pin is never in a floating state

## Slide 6: Download led_button.ino
Notice:
If button is
  Pressed
    digitalRead() returns HIGH
  Not being pressed
    digitalRead() returns LOW
When did you have to last hold the button down to keep a light on?

## Slide 7: Bouncy buttons
Bouncy button means when you press the button the volatge bounces up and down before it settles to the high state.
This would turn something on and off several times.
We can program a small delay to help combat this issue.

## Slide 8: Download debounce.ino
Upload to the Uno and test the button for bounciness

## Slide 9: How it works
Stores the state of the button
  Initialized to LOW
Reads the current state
If the current state differs from the previous state
  Waits 5 ms (button must have changed states)
  Rereads the button and uses that as the current state
If the previous state was low and current state is high
  Toggles the led state
Set the previous button state to the current button state
Repeats from step 2

## Slide 10: Diagram

## Slide 11: Download RGB_nightlight.ino
Download from the github page.
Upload to Arduino and test its function.

## Slide 12: Reading Analog Sensors

## Slide 13: Why we still need analog in a “digital world”?
Observable features are analog
  they can assume any number of potential states
    Color of sunlight
    Temperature
    Concentration of contaminants in the air
So we need a way to distinguish between analog and digital inputs and convert between the two

## Slide 14: Analog to digital converter (ADC)
Suppose you want to measure the brightness of the room (measured in lux - it could be any decimal from 0 to ∞)
Pitch black - output 0 volts
Completely saturated - outputs 5 volts
Half saturated - outputs 4.5 volts
⅓ saturated - outputs 1.6666 volts
etc.
You need to use the analog to digital converter (ADC) built into the Arduino to read this value

## Slide 15: But what is a ADC doing?
In the Arduino
  10-bit ADC
    This means that the ADC can subdivide (or quantize) an analog signal into 210 different values
      210 = 1024
    So from the reference voltage (5 v)
      2.5 v is mapped to 512 (½ of 1024)
      1.25 v is mapped to 256 (¼ of 1024)
      etc.

## Slide 16: Visual of what’s happening
Here is a 2 bit ADC, it has 2 bits of resolution and therefore 4 total logic levels (22 = 4)
The higher the resolution the more “steps” in the digitized signal (remember the Arduino has 10 bit resolution… so 1024 steps)

## Slide 17: Reading analog signals
Let's start with a potentiometer
  Pot for short
  Used in
    car stereos
    Thermostats
    speakers
    Etc.
  3 pins
    Outer is grounded (symmetrical so it doesn't matter which side)
    Other side pin is connected to high (5 v)
    Inner pin is connected to ADC input – The output
  As you turn the knob you are changing the resistance and thus the output voltage (by ohm's law) to any value between 0 v and 5 v

## Slide 18: Lets wire up a circuit

## Slide 19: Download pot.ino from github and upload

## Slide 20: Notice the new functions
analogRead()
  This function reads the value of the analog pin connected to the Arduino
Serial.println()
  This function prints to the Arduino IDE serial monitor
serial.begin()
  In the setup section
  Takes an argument that specifies the communication rate (baud rate)
    Faster baud = more data in less time
      Can induce transmission error
    9600 is common value (and will be the standard we use)

## Slide 21: What you should see
The TX LED on the Arduino should be blinking every 500 ms
  This indicated the Arduino is transmitting data
After launching the serial monitor you should see a window w/ numbers streaming by
  Turning the dial the numbers should go up and down (corresponding to the position of the potentiometer)
    One way goes toward 0
    The other towards 1023
  If you are getting “funky data” you need to ensure the baud rate is correctly set on the monitor
Serial Monitor

## Slide 22: Use an analog sensor to sense temperature

## Slide 23: Wire it up

## Slide 24: Before we can begin
We need cut offs
  Using the same concepts as before we can find
    Launch the sketch from before and see what “room temp” corresponds to
      When writing this 200 C was about 143 (these will be different for you)
    Do a bit of math
    5V / 1024 is 0.00488. So for every 0.0048V you get 1 DAC value increase.
    20°/143 is 0.1399. So each degree Celsius correspondes to 0.1399/.0048 or ~30 DAC values
    So to make the green LED light turn on, subtract 60 DAC values and add to the code
    To make the RED LED light turn on, add 60 DAC values and add to the code

## Slide 25: Try it yourself first
Goal to get to
  Try to write a code that
    When the temperature is with in “room temp” ± 2 0C the led is Green
    If the temp is lower than that the LED is Blue
    If the temp is higher than that the LED is Red

## Slide 26: Download tempalert.ino from github

## Slide 27: Add the Photoresistor
Insert the Photo Diode into Analog In 0

## Slide 28: Download nightlight from github

## Slide 29: New function
map()
Output = map(value, fromLow, fromHigh, toLow, toHigh)
  Value - the information you start with
    Most recent reading from analog input
  fromLow and fromHigh
    Input boundaries
      Min and Max brightness
  toLow and toHigh
      Values you want to map to
        255 and 0 (swapped to turn off the light when bright)
constrain()
constrain(value, min, max)
  Constrains the value given between 2 values
    If the photo resistor measured to high you would pass below 0 (its inverted to turn off in light)

## Slide 30: Stay tuned
Arduino 3 will cover Motors and Servos.
We’ll use Motors, H-bridges and Servos!